## Slide 1: Lab4 Intro Creating a Processor System

## Slide 2: Objectives
After completing this lab, you will be able to:
  Understand the steps and directives involved in creating an s_axilite IP-XACT hardware accelerator from a synthesized design in Vitis HLS
  Create a processor system using IP Integrator in Vivado
  Integrate the generated s_axilite IP-XACT hardware accelerator into the created processor system

## Slide 3: The Design
The design consists of a FIR filter to filter a 4 KHz tone added to a CD quality (48 KHz) music. This lab requires you to develop a peripheral core of the designed filter that can be instantiated in a processor system. The processor system will acquire a stereo music using on-board ADAU1761 CODEC chip from Analog Devices and I2S controller, process (bandstop filter) it through the designed filter, and output back to the speaker

## Slide 4: Procedure
Create a Vitis HLS project for the FIR filter
Run simulation and verify functionality
Synthesize the design
Run RTL/C Co-simulation
Setup IP-XACT hardware accelerator
Generate the IP-XACT hardware accelerator
Create a Vitis project
Generate bitstream and export to SDK
Generate an application
Verify in hardware

## Slide 5: Summary
In this lab, you added RESOURCE directive to create an s_axilite IP-XACT hardware accelerator. You generated the s_axilite IP-XACT hardware accelerator. You then created a processor system using IP Integrator, integrated the generated ip core, and tested the system with the provided application