## Slide 1: Using Vitis HLS
XUP

## Slide 2: Objectives
After completing this module, you will be able to:
  List various OS under which Vitis HLS is supported
  Describe how projects are created and maintained in Vitis HLS
  State various steps involved in using Vitis HLS project creation wizard
  Distinguish between the role of top-level module in testbench and design to be synthesized
  List various verifications which can be done in Vitis HLS
  List Vitis HLS project directory structure

## Slide 3: Outline
Invoking Vitis HLS
Project Creation using Vitis HLS
Synthesis to IPXACT Flow
Design Analysis
Other Ways to use Vitis HLS
Summary

## Slide 4: Invoke Vitis HLS from the terminal
12- 4
The first step is to open or create a project

## Slide 5: Invoke Vivado HLS from Windows Menu
The first step is to open or create a project
12- 5

## Slide 6: Vitis HLS GUI
Information
Pane
Project
Explorer
Pane
12- 6
Auxiliary Pane
Console
Pane

## Slide 7: Vivado HLS GUI
Information
Pane
Project
Explorer
Pane
12- 7
Auxiliary Pane
Console
Pane

## Slide 8: Project Creation using Vitis HLS

## Slide 9: Vitis HLS Projects and Solutions
Vitis HLS is project based
  A project specifies the source code which will be synthesized
  Each project is based on one set of source code
  Each project has a user specified name
A project can contain multiple solutions
  Solutions are different implementations of the same code
  Auto-named solution1, solution2, etc.
  Supports user specified names
  Solutions can have different clock frequencies, target technologies, synthesis directives
Projects and solutions are stored in a hierarchical directory structure
  Top-level is the project directory
  The disk directory structure is identical to the structure shown in the GUI project explorer (except for source code location)
Project Level
Source
Solution Level
12- 9

## Slide 10: Vivado HLS Projects and Solutions
Vivado HLS is project based
  A project specifies the source code which will be synthesized
  Each project is based on one set of source code
  Each project has a user specified name
A project can contain multiple solutions
  Solutions are different implementations of the same code
  Auto-named solution1, solution2, etc.
  Supports user specified names
  Solutions can have different clock frequencies, target technologies, synthesis directives
Projects and solutions are stored in a hierarchical directory structure
  Top-level is the project directory
  The disk directory structure is identical to the structure shown in the GUI project explorer (except for source code location)
Project Level
Source
Solution Level
12- 10

## Slide 11: Vitis HLS Step 1: Create or Open a project
Start a new project
  The GUI will start the project wizard to guide you through all the steps
Open an existing project
  All results, reports and directives are automatically saved/remembered
  Use “Recent Project” menu for quick access
Optionally use the Toolbar Button to
Open Project
12- 11

## Slide 12: Vivado HLS Step 1: Create or Open a project
Start a new project
  The GUI will start the project wizard to guide you through all the steps
Open an existing project
  All results, reports and directives are automatically saved/remembered
  Use “Recent Project” menu for quick access
Optionally use the Toolbar Button to
Open New Project
12- 12

## Slide 13: Project Wizard
The Project Wizard guides users through the steps of opening a new project
Define project and directory
Add design source files
Specify test bench files
Specify clock and select part
Step-by-step guide …
Project Level Information
1st Solution Information

## Slide 14: Project Wizard
The Project Wizard guides users through the steps of opening a new project
Define project and directory
Add design source files
Specify test bench files
Specify clock and select part
Step-by-step guide …
Project Level Information
1st Solution Information

## Slide 15: Define Project & Directory
Define the project name
Browse to the location of the project
  In this example, project directory “matrixmul” will be created inside directory “lab1”

## Slide 16: Define Project & Directory
Define the project name
  Note, here the project is given the extension .prj
  A useful way of seeing it’s a project (and not just another directory) when browsing
Browse to the location of the project
  In this example, project directory “matrixmul.prj” will be created inside directory “lab1”

## Slide 17: Add Design Source Files
Add Design Source Files
  This allows Vitis HLS to determine the top-level design for synthesis, from the test bench and associated files
Add Files…
  Select the source code file(s)
  The CTRL and SHIFT keys can be used to add multiple files
  No need to include headers (.h) if they reside in the same directory
Select File and Edit CFLAGS…
  If required, specify C compile arguments using the “Edit CFLAGS…”
    Define macros: -DVERSION1
    Location of any (header) files not in the same directory as the source: -I../include
There is no need to add the location of standard Vitis HLS header files or header files located in the same project location

## Slide 18: Add Design Source Files
Add Design Source Files
  This allows Vivado HLS to determine the top-level design for synthesis, from the test bench and associated files
  Not required for SystemC designs
Add Files…
  Select the source code file(s)
  The CTRL and SHIFT keys can be used to add multiple files
  No need to include headers (.h) if they reside in the same directory
Select File and Edit CFLAGS…
  If required, specify C compile arguments using the “Edit CFLAGS…”
    Define macros: -DVERSION1
    Location of any (header) files not in the same directory as the source: -I../include
There is no need to add the location of standard Vivado HLS or SystemC header files or header files located in the same project location

## Slide 19: Specify Test Bench Files
Use “Add Files” to include the test bench
  Vitis HLS will re-use these to verify the RTL using co-simulation
And all files referenced by the test bench
  The RTL simulation will be executed in a different directory (Ensures the original results are not over-written)
  Vitis HLS needs to also copy any files accessed by the test bench
    E.g. Input data and output results
Add Folders
  If the test bench uses relative paths like “sub_directory/my_file.dat” you can add “sub_directory” as a folder/directory
Use “Edit CFLAGS…”
  To add any C compile flags required for compilation

## Slide 20: Specify Test Bench Files
Use “Add Files” to include the test bench
  Vivado HLS will re-use these to verify the RTL using co-simulation
And all files referenced by the test bench
  The RTL simulation will be executed in a different directory (Ensures the original results are not over-written)
  Vivado HLS needs to also copy any files accessed by the test bench
    E.g. Input data and output results
Add Folders
  If the test bench uses relative paths like “sub_directory/my_file.dat” you can add “sub_directory” as a folder/directory
Use “Edit CFLAGS…”
  To add any C compile flags required for compilation

## Slide 21: Test benches I
The test bench should be in a separate file
Or excluded from synthesis
  The Macro __SYNTHESIS__ can be used to isolate code which will not be synthesized
    This macro is defined when Vitis HLS parses any code (-D__SYNTHESIS__)
// test.c
#include <stdio.h>
void test (int d[10]) {
int acc = 0;
int i;
for (i=0;i<10;i++) {
acc += d[i];
d[i] = acc;
}
}
#ifndef __SYNTHESIS__
int main () {
int d[10], i;
for (i=0;i<10;i++) {
d[i] = i;
}
test(d);
for (i=0;i<10;i++) {
printf("%d %d\n", i, d[i]);
}
return 0;
}
#endif
Design to be synthesized
Test Bench
Nothing in this ifndef will be read by Vitis HLS
(will be read by gcc)

## Slide 22: Test benches II
Ideal test bench
  Should be self checking
    RTL verification will re-use the C test bench
  If the test bench is self-checking
    Allows RTL Verification to be run without a requirement to check the results again
  RTL verification “passes” if the test bench return value is 0 (zero)
    Actively return a 0 if the simulation passes
  Non-synthesizable constructs may be added to a synthesize function if __SYNTHESIS__ is used
int main () {
// Compare results
int ret = system("diff --brief -w test_data/output.dat test_data/output.golden.dat");
if (ret != 0) {
printf("Test failed !!!\n", ret); return 1;
} else {
printf("Test passed !\n", ret); return 0;
}
The –w option ensures the “newline” does not cause a difference between Windows and Linux files
#ifndef __SYNTHESIS__
image_t *yuv = (image_t *)malloc(sizeof(image_t));
#else // Workaround malloc() calls w/o changing rest of code
image_t _yuv;
#endif

## Slide 23: Solution Configuration
Provide a solution name
  Default is solution1, then solution2 etc.
Specify the clock
  The clock uncertainty is subtracted from the clock to provide an “effective clock period”
  Vitis HLS uses the “effective clock period” for Synthesis
  Provides users defined margin for downstream RTL synthesis, P&R
Select the part
  Select a device family after applying filters such as family, package and speed grade (see next slide) or a board after applying boards specify

## Slide 24: Solution Configuration
Provide a solution name
  Default is solution1, then solution2 etc.
Specify the clock
  The clock uncertainty is subtracted from the clock to provide an “effective clock period”
  Vivado HLS uses the “effective clock period” for Synthesis
  Provides users defined margin for downstream RTL synthesis, P&R
Select the part
  Select a device family after applying filters such as family, package and speed grade (see next slide) or a board after applying boards specify

## Slide 25: Selecting Part and Implementation Engine
Select the target part either through Parts or Boards specify

## Slide 26: Selecting Part and Implementation Engine
Select the target part either through Parts or Boards specify
Select RTL Tools
  Auto
    Will select Vivado for 7 Series and Zynq devices
    Will select ISE for Virtex-6 and earlier families
  Vivado
  ISE
    ISE Design Suite must be installed and must be included in the PATH variable

## Slide 27: Clock Specification
Clock frequency must be specified
  Only 1 clock can be specified for C/C++ functions
Clock uncertainty can be specified
  Subtracted from the clock period to give an effective clock period
  The effective clock period is used for synthesis
    Should not be used as a design parameter
    Do not vary for different results: this is your safety margin
  A user controllable margin to account for downstream RTL synthesis and P&R
Clock Period
Clock Uncertainty
Effective Clock Period
used by Vitis HLS
Margin for Logic Synthesis and P&R

## Slide 28: A Vitis HLS Project
Console Pane
Displays Vitis HLS run time messages
Project Explorer
Project files displayed in a hierarchal view
Information Pane
Can view and edit any file from the Project Explorer
Auxiliary Pane
Cross-referenced with the Information Pane (here it shows objects in the source code)

## Slide 29: A Vivado HLS Project
Console Pane
Displays Vivado HLS run time messages
Project Explorer
Project files displayed in a hierarchal view
Information Pane
Can view and edit any file from the Project Explorer
Auxiliary Pane
Cross-referenced with the Information Pane (here it shows objects in the source code)

## Slide 30: Vitis HLS GUI Toolbar
The primary commands have toolbar buttons
  Easy access for standard tasks
  Button highlights when the option is available
    E.g. cannot perform C/RTL simulation before synthesis
Open a Project
Create a new Solution
Change Solution Settings
Change Project Settings
Open Schedule Viewer
Run C Synthesis
Export RTL
Run C Simulation
Open Reports
Run C/RTL Cosimulation

## Slide 31: Vivado HLS GUI Toolbar
The primary commands have toolbar buttons
  Easy access for standard tasks
  Button highlights when the option is available
    E.g. cannot perform C/RTL simulation before synthesis
Create a new Project
Create a new Solution
Change Solution Settings
Change Project Settings
Run C Simulation
Run C Synthesis
Export RTL
Open Reports
Open Analysis Viewer
Compare Reports
Run C/RTL Cosimulation

## Slide 32: Files: Views, Edits & Information
Open file and it will display in the information pane
The Auxiliary pane is context sensitive with respect to the information pane
Here it displays elements in the code which can have directives specified on them

## Slide 33: Files: Views, Edits & Information
Open file and it will display in the information pane
The Auxiliary pane is context sensitive with respect to the information pane
Here it displays elements in the code which can have directives specified on them

## Slide 34: Synthesis to IPXACT Flow

## Slide 35: Synthesis
Run C Synthesis
Console
  Will show run time information
  Examine for failed constraints
A “syn” directory is created
  Verilog & VHDL RTL
  Synthesis reports for all non-inlined functions
Report opens automatically
  When synthesis completes
Report is outlined in the Auxiliary pane

## Slide 36: Synthesis
Run C Synthesis
Console
  Will show run time information
  Examine for failed constraints
A “syn” directory is created
  Verilog, VHDL & SystemC RTL
  Synthesis reports for all non-inlined functions
Report opens automatically
  When synthesis completes
Report is outlined in the Auxiliary pane

## Slide 37: Vitis HLS : RTL Verification
Vitis Development
Environment
RTL output in Verilog and VHDL
Automatic re-use of the C-level test bench
Support for Xilinx simulators (XSim and ISim) and 3rd party HDL simulators in automated flow
RTL verification can be executed from within Vitis HLS
Validate C
Verify RTL
Vitis
Vitis Model Composer

## Slide 38: RTL Verification: Under-the-Hood
RTL Co-Simulation
  Vitis HLS provides RTL verification
  Creates the wrappers and adapters to re-use the C test bench
Prior to synthesis
  Test bench
  Top-level C function
After synthesis
  Test bench
  Wrapper created by Vitis HLS
  Adapters created by Vitis HLS
  RTL output from Vitis HLS
    Verilog or VHDL
There is no HDL test bench created
12- 38
main.c(pp)
dut.c(pp)
main.c(pp)
RTL
Adapter
Adapter
Synthesis
DUT wrapper

## Slide 39: C/RTL Co-simulation
Start Simulation
  Opens the dialog box
Select the RTL
  Verilog and VHDL require the appropriate simulator
    Select the desired simulator
Options
  Can output trace file (VCD format)
  Optimize the C compilation & specify test bench linker flags
  The “setup only” option will not execute the simulation
OK will run the simulator
  Output files will be created in a “sim” directory

## Slide 40: C/RTL Co-simulation
Start Simulation
  Opens the dialog box
Select the RTL
  Verilog and VHDL require the appropriate simulator
    Select the desired simulator
Options
  Can output trace file (VCD format)
  Optimize the C compilation & specify test bench linker flags
  The “setup only” option will not execute the simulation
OK will run the simulator
  Output files will be created in a “sim” directory

## Slide 41: Simulation Results
Simulation output is shown in the console
Expect the same test bench response
  If the C test bench plots, it will with the RTL design (but slower)
Sim Directory
  Will contain a sub-directory for each RTL which is verified
Report
  A report is created and opened automatically

## Slide 42: Simulation Results
Simulation output is shown in the console
Expect the same test bench response
  If the C test bench plots, it will with the RTL design (but slower)
Sim Directory
  Will contain a sub-directory for each RTL which is verified
Report
  A report is created and opened automatically

## Slide 43: Vitis HLS : RTL Export
RTL output in Verilog, VHDL
Scripts created for RTL synthesis tools
IP-XACT and SysGen => Vitis HLS for 7 Series and Zynq families
PCore => Only Vitis HLS Standalone for all families
RTL Export to IP-XACT, SysGen, and Pcore formats
Vitis

## Slide 44: Vivado HLS : RTL Export
RTL output in Verilog, VHDL and SystemC
Scripts created for RTL synthesis tools
IP-XACT and SysGen => Vivado HLS for 7 Series and Zynq families
PCore => Only Vivado HLS Standalone for all families
RTL Export to IP-XACT, SysGen, and Pcore formats

## Slide 45: RTL Export Support
RTL Export
  Can be exported to one of the two types
    IP-XACT formatted IP for use with Vitis System Edition (SE)
      7 Series and Zynq families only; supported by HLS and VITIS_HLS licenses
    A System Generator IP block
      7 Series and Zynq families only; supported by HLS and VITIS_HLS licenses
Generation in both Verilog and VHDL for non-bus or non-interface based designs
Logic synthesis will automatically be performed
  HLS license will use Vitis RTL Synthesis
12- 45

## Slide 46: RTL Export: Synthesis
RTL Synthesis can be performed to evaluate the RTL
  IP-XACT and System Generator formats: Vitis synthesis performed
  Pcore format: Vitis synthesis is performed
RTL synthesis results are not included with the IP package
  Evaluate step is provided to give confidence
    Timing will be as estimate (or better)
    Area will be as estimated (or better)
  Final RTL IP is synthesized with the rest of the RTL design
    RTL Synthesis results from the Vitis HLS evaluation are not used
project.prj
impl
verilog
vhdl
sim
solutionN
solution1
ip
sysgen
syn
IP Repositories
RTL Synthesis Results

## Slide 47: RTL Export: IP Repositories
IP can be imported into other Xilinx tools
project.prj
impl
sim
solutionN
solution1
ip
sysgen
syn
In Vitis :
Project Manager > IP Catalog
Add IP to import this block
Browse to the zip file inside “ip”
In System Generator :
Use XilinxBlockAdd
Select Vitis_HLS block type
Browse to the solution directory
Project Directory
Top-level project directory
(there must be one)
Solution directories
There can be multiple solutions for each project. Each solution is a different implementation of the same (project) source code

## Slide 48: RTL Export for Implementation
Click on Export RTL
  Export RTL Dialog opens
Select the desired output format
Optionally, configure the output
Select the desired language
Optionally, click on implementation and choose RTL Synthesis, Place & Route options for invoking implementation tools from within Vitis HLS
Click OK to start the implementation

## Slide 49: RTL Export for Implementation
Click on Export RTL
  Export RTL Dialog opens
Select the desired output format
Optionally, configure the output
Select the desired language
Optionally, click on Vivado RTL Synthesis and Place and Route options for invoking implementation tools from within Vivado HLS
Click OK to start the implementation

## Slide 50: RTL Export (Place and Route Option) Results
Impl directory created
  Will contain a sub-directory for each RTL which is synthesized
Report
  A report is created and opened automatically

## Slide 51: RTL Export (Place and Route Option) Results
Impl directory created
  Will contain a sub-directory for each RTL which is synthesized
Report
  A report is created and opened automatically

## Slide 52: RTL Export Results (Place and Route Option Unchecked)
Impl directory created
  Will contain a sub-directory for both VHDL and Verilog along with the ip directory
No report will be created
Observe the console
  No packing, routing phases

## Slide 53: RTL Export Results (Place and Route Option Unchecked)
Impl directory created
  Will contain a sub-directory for both VHDL and Verilog along with the ip directory
No report will be created
Observe the console
  No packing, routing phases

## Slide 54: Design Analysis

## Slide 55: Analysis Perspective
Perspective for design analysis
  Allows interactive analysis

## Slide 56: Performance Analysis

## Slide 57: Performance Analysis

## Slide 58: Resources Analysis

## Slide 59: Resources Analysis

## Slide 60: Function Call Graph

## Slide 61: Other Ways to use Vitis HLS

## Slide 62: Command Line Interface: Batch Mode
Vivado HLS can also be run in batch mode
  Opening the Command Line Interface (CLI) will give a shell
  Supports the commands required to run Vivado HLS & pre-synthesis verification (gcc, g++, apcc, make)
12- 62

## Slide 63: Using Vitis HLS CLI
Invoke Vitis HLS in interactive mode
  Type Tcl commands one at a time
Execute Vitis HLS using a Tcl batch file
  Allows multiple runs to be scripted and automated
Open an existing project in the GUI
  For analysis, further work or to modify it
Use the terminal to launch Vitis HLS GUI
12- 63
> vitis_hls –i
> vitis_hls –p my.prj
> vitis_hls –f run_aesl.tcl
> vitis_hls

## Slide 64: Using Tcl Commands
When the project is created
  All Tcl command to run the project are created in script.tcl
    User specified directives are placed in directives.tcl
  Use this as a template from creating Tcl scripts

## Slide 65: Using Tcl Commands
When the project is created
  All Tcl command to run the project are created in script.tcl
    User specified directives are placed in directives.tcl
  Use this as a template from creating Tcl scripts
    Uncomment the commands before running the Tcl script

## Slide 66: Help
Help is always available
  The Help Menu
  Opens User Guide, Reference Guide and Man Pages
In interactive mode
  The help command lists the man page for all commands
Auto-Complete all commands using the tab key

## Slide 67: Help
Help is always available
  The Help Menu
  Opens User Guide, Reference Guide and Man Pages
In interactive mode
  The help command lists the man page for all commands
Vivado_hls> help add_files
SYNOPSIS
add_files [OPTIONS] <src_files>
Etc…
Auto-Complete all commands using the tab key

## Slide 68: Summary

## Slide 69: Summary
Vitis HLS can be run under Windows 10, Red Hat Linux, Cent OS, and Ubuntu
Vitis HLS can be invoked through GUI and command line in Windows OS, and command line in Linux
Vitis HLS project creation wizard involves
  Defining project name and location
  Adding design files
  Specifying testbench files
  Selecting clock and technology
The top-level module in testbench is main() whereas top-level module in the design is the function to be synthesized
12- 69

## Slide 70: Summary
Vivado HLS can be run under Windows 7/8.1/10, Red Hat Linux, SUSE OS, and Ubuntu
Vivado HLS can be invoked through GUI and command line in Windows OS, and command line in Linux
Vivado HLS project creation wizard involves
  Defining project name and location
  Adding design files
  Specifying testbench files
  Selecting clock and technology
The top-level module in testbench is main() whereas top-level module in the design is the function to be synthesized
12- 70

## Slide 71: Summary
Vitis HLS project directory consists of
  *.prj project file
  Multiple solutions directories
  Each solution directory may contain
    impl, synth, and sim directories
    The impl directory consists of ip, verilog, and vhdl folders
    The synth directory consists of reports, vhdl, and verilog folders
    The sim directory consists of testbench and simulation files