## Slide 1: Creating Processor System
XUP

## Slide 2: Objectives
After completing this module, you will be able to:
  Describe embedded system development flow in Zynq
  List the steps involved in creating hardware accelerator
  State how hardware accelerator created in Vitis HLS is used in Vivado Design Suite

## Slide 3: Outline
Embedded System Design in Zynq using IP Integrator
Creating IP-XACT Hardware Accelerator
Integrating the IP-XACT Hardware Accelerator in AXI System
Summary

## Slide 4: Embedded Design Architecture in Zynq
Embedded design in Zynq is based on:
  Processor and peripherals
    Dual ARM® Cortex™ -A9 processors of Zynq-7000 SoC
    AXI interconnect
    AXI component peripherals
    Reset, clocking, debug ports
  Software platform for processing system
    Standalone OS
    C language support
    Processor services
    C drivers for hardware
  User application
    Interrupt service routines (optional)

## Slide 5: The PS and the PL
The Zynq-7000 SoC architecture consists of two major sections
  PS: Processing system
    Single/Dual ARM Cortex-A9 processor based (Single core versions available)
    Multiple peripherals
    Hard silicon core
  PL: Programmable logic
    Uses the same 7 series programmable logic

## Slide 6: Vivado
What are Vivado, IP Integrator and Vitis?
  Vivado is the tool suite for Xilinx FPGA design and includes capability for embedded system design
    IP Integrator, is part of Vivado and allows block level design of the hardware part of an Embedded system
    Vivado includes all the tools, IP, and documentation that are required for designing systems with the Zynq-7000 SoC hard core and/or Xilinx MicroBlaze soft core processor
    Vivado + IPI replaces ISE/EDK
  Vitis core development kit includes comprehensive developer tools to design, debug, and deploy software applications targeted towards embedded processors
    Xilinx Zynq, MPSoC, RFSoC, and ACAP devices.
Vivado is the overall project manager and is used for developing non-embedded hardware and instantiating embedded systems
  Vivado/IP Integrator flow is recommended for developing Zynq embedded systems

## Slide 7: Vivado
What are Vivado, IP Integrator and SDKVitis?
  Vivado is the tool suite for Xilinx FPGA design and includes capability for embedded system design
    IP Integrator, is part of Vivado and allows block level design of the hardware part of an Embedded system
    Integrated into Vivado
    Vivado includes all the tools, IP, and documentation that are required for designing systems with the Zynq-7000 SoC hard core and/or Xilinx MicroBlaze soft core processor
    Vivado + IPI replaces ISE/EDK
  Vitis core development kit includes comprehensive developer tools to design, debug, and deploy software applications targeted towards embedded processors
    Xilinx Zynq, MPSoC, RFSoC, and ACAP devices.
  SDK is an Eclipse-based software design environment
    Enables the integration of hardware and software components
    Links from Vivado
Vivado is the overall project manager and is used for developing non-embedded hardware and instantiating embedded systems
  Vivado/IP Integrator flow is recommended for developing Zynq embedded systems

## Slide 8: Embedded System Tools: Hardware
Hardware development tools
  IP Integrator
  IP Packager
  Hardware netlist generation
  Simulation model generation
  Hardware debugging using Vivado analyzer cores

## Slide 9: Embedded System Tools: Software
Vitis Unified Software Platform
  Board support package creation
  GNU software development tools
  C/C++ compiler for the MicroBlaze and ARM Cortex-A9 processors (gcc)
  Debugger for the MicroBlaze and ARM Cortex-A9 processors (system debugger)
  TCF framework – multicore debug
  Feature
    Importing target platform definition created using Vivado® Design Suite
    Application development for single, multi-processor and heterogenous processor systems
    Ability to create and configure board support packages (BSPs) for third-party OS
    Board bring-up and Firmware development
    System-level performance analysis and benchmarking
    Real-time debug and trace of heterogeneous embedded systems

## Slide 10: Embedded System Tools: Software
Eclipse IDE-based Software Development Kit (SDK)
  Board support package creation
  GNU software development tools
  C/C++ compiler for the MicroBlaze and ARM Cortex-A9 processors (gcc)
  Debugger for the MicroBlaze and ARM Cortex-A9 processors (system debugger)
  TCF framework – multicore debug
Board support packages (BSPs)
  Stand-alone BSP
    Free basic device drivers and utilities from Xilinx
    NOT an RTOS

## Slide 11: Vivado View
Customizable panels
  A: Project Management
  B: IP Integrator
  C: FPGA Flow
  D: Layout Selection
  E: Project view/Preview Panel
  F: Console, Messages, Logs
A
B
C
D
E
F

## Slide 12: Vivado View
Customizable panels
  A: Project Management
  B: IP Integrator
  C: FPGA Flow
  D: Layout Selection
  E: Project view/Preview Panel
  F: Console, Messages, Logs
A
B
C
D
E
F

## Slide 13: Embedded System Design using Vivado
15. Program bitstream & .elf into Zynq
Vivado
VITS
1. Launch Vivado
2. Create Block Design
8. Create Top-Level HDL
9. Add Constraints (file)
10. Generate Bitstream => .bit
11. Export hardware to VITIS
3. Add PS7
4. Configure PS settings
5. Run Block Automation
6. Add and configure IPs
7. Run Connection Automation
12. Create platform project from XSA
13. Create or add Software Project
14. Build application => .elf
PYNQ-Z1
IP Integrator
PYNQ-Z2

## Slide 14: Embedded System Design using Vivado
15. Program bitstream & .elf into Zynq
Vivado
VITS
1. Launch Vivado
2. Create Block Design
8. Create Top-Level HDL
9. Add Constraints (file)
10. Generate Bitstream => .bit
11. Export hardware to VITIS
3. Add PS7
4. Configure PS settings
5. Run Block Automation
6. Add and configure IPs
7. Run Connection Automation
12. Create Board Support Package
12. Create platform project from XSA
13. Create or add Software Project
14. Build application => .elf
PYNQ-Z1
IP Integrator
PYNQ-Z2

## Slide 15: Add IP Integrator Block Diagram
IP Integrator Block Diagram opens a blank canvas
IP can be added from the IP catalog
Drag and drop interface
Intelligent Design environment
  Design Assistance
  Connection automation
  Highlights valid connections
  Group, create hierarchal blocks
Can import custom IP using IP Packager

## Slide 16: Add IP Integrator Block Diagram
IP Integrator Block Diagram opens a blank canvas
IP can be added from the IP catalog
Drag and drop interface
Intelligent Design environment
  Design Assistance
  Connection automation
  Highlights valid connections
  Group, create hierarchal blocks
Can import custom IP using IP Packager

## Slide 17: Configuring and Connecting Hardware in IP Integrator
Double click blocks to access configuration options
Drag pointer to make connections
  Highlights valid connections
Connection Automation
  Automatically connect recognised interfaces
Automatically redraw system

## Slide 18: Add IP Integrator Block Diagram
IP Integrator Block Diagram opens a blank canvas
IP can be added from the IP catalog
Drag and drop interface
Intelligent Design environment
  Design Assistance
  Connection automation
  Highlights valid connections
  Group, create hierarchal blocks
Can import custom IP using IP Packager

## Slide 19: Exporting to VITIS
Export hardware platform first
  The XSA file has the hardware specifications like processor configuration properties, peripheral connection information, address map, and device initialization code.
  Include bitstream if generated
Launch VITIS
  Software development is performed with the Vitis Unified Software Platform
The VITIS tool will then associate user software projects to hardware

## Slide 20: Exporting to VITIS
Export hardware platform first
  The Hardware Description File (hdf) format file containing all the relevant information will be created and placed under the *.sdk directory
  The XSA file has the hardware specifications like processor configuration properties, peripheral connection information, address map, and device initialization code.
  Include bitstream if generated
Launch XSDKVITIS
  Software development is performed with the Xilinx Software Development Kit tool (XSDK)
  Software development is performed with the Vitis Unified Software Platform
The XSDKVITIS tool will then associate user software projects to hardware

## Slide 21: Software Development Flow
Create/Import platform project
  Import Hardware Spec from XSA to Vitis
  Domain Creation
Create software application
Update linker script, if needed
Build project
  compile, assemble, link output file <app_project>.elf

## Slide 22: Software Development Flow
Create/Import hardware platform project
  Automatically performed when XSDK tool is launched from Vivado project
  Import Hardware Spec from XSA to Vitis
  Domain Creation
Create BSP
  System software, board support package
Create software application
Update linker script, if needed
Build project
  compile, assemble, link output file <app_project>.elf

## Slide 23: Creating IP-XACT Hardware Accelerator

## Slide 24: Port-Level Interfaces
The AXI4 interfaces supported by Vitis HLS include
  The AXI4-Stream (axis)
    Specify on input arguments or output arguments only, not on input/output arguments
  The AXI4 master (m_axi)
    Specify on arrays and pointers (and references in C++) only. You can group multiple arguments into the same AXI4 interface using the bundle option
  The AXI4-Lite (s_axilite)
    Specify an AXI4-Lite slave I/O protocol on any type of argument except streams. You can group multiple arguments into the same AXI4-Lite interface using the bundle option

## Slide 25: Port-Level Interfaces
The AXI4 interfaces supported by Vitis HLS include
  The AXI4-Stream (axis)
    Specify on input arguments or output arguments only, not on input/output arguments
  The AXI4 master (m_axi)
    Specify on arrays and pointers (and references in C++) only. You can group multiple arguments into the same AXI4-LiteAXI4 interface using the bundle option
  The AXI4-Lite (s_axilite)
    Specify on any type of argument except arrays. Specify an AXI4-Lite slave I/O protocol on any type of argument except streams. You can group multiple arguments into the same AXI4-Lite interface using the bundle option

## Slide 26: Interface Modes
Native AXI Interfaces
  AXI4 Slave Lite, AXI4 Master, AXI Stream supported by INTERFACE directive
    Provided in RTL after Synthesis
    Supported by C/RTL Co-simulation
    Supported for Verilog and VHDL
BRAM Memory Interface
  Identical IO protocol to ap_memory
  Bundled differently in IP Integrator
    Provides easier integration to memories with BRAM interface
No IO Protocol
Block Level Protocol
AXI4 Interfaces
Wire handshake
protocols
Memory protocols
: RAM
: FIFO

## Slide 27: Interface Modes
Native AXI Interfaces
  AXI4 Slave Lite, AXI4 Master, AXI Stream supported by INTERFACE directive
    Provided in RTL after Synthesis
    Supported by C/RTL Co-simulation
    Supported for Verilog and VHDL
BRAM Memory Interface
  Identical IO protocol to ap_memory
  Bundled differently in IP Integrator
    Provides easier integration to memories with BRAM interface
axis
s_axilite
m_axi
bram
No IO Protocol
Block Level Protocol
AXI4 Interfaces
Wire handshake
protocols
Memory protocols
: RAM
: FIFO

## Slide 28: Native AXI Slave Lite Interface
Interface Mode: s_axilite
  Supported with INTERFACE directive
  Multiple ports may be grouped into the same Slave Lite interface
    All ports which use the same bundle name are grouped
Grouped Ports
  Default mode is ap_none for input ports
  Default mode is ap_vld for output ports
  Default mode ap_ctrl_hs for function return
  Default mode can be changed with additional INTERFACE directives
void example(char *a, char *b, char *c)
{
#pragma HLS INTERFACE mode=s_axilite port=a bundle=BUS_A
#pragma HLS INTERFACE mode=s_axilite port=b bundle=BUS_A
#pragma HLS INTERFACE mode=s_axilite port=c bundle=OUT
#pragma HLS INTERFACE mode=s_axilite port=return bundle=BUS_A
#pragma HLS INTERFACE mode=ap_vld port=b
*c += *a + *b;
}
Notes: Ug1399 Page 264 S_AXILITE and Port-Level Protocols

## Slide 29: Native AXI Slave Lite Interface
Interface Mode: s_axilite
  Supported with INTERFACE directive
  Multiple ports may be grouped into the same Slave Lite interface
    All ports which use the same bundle name are grouped
Grouped Ports
  Default mode is ap_none for input ports
  Default mode is ap_vld for output ports
  Default mode ap_ctrl_hs for function return
  Default mode can be changed with additional INTERFACE directives
void example(char *a, char *b, char *c)
{
#pragma HLS INTERFACE s_axilite port=return bundle=BUS_A
#pragma HLS INTERFACE s_axilite port=a bundle=BUS_A
#pragma HLS INTERFACE s_axilite port=b bundle=BUS_A
#pragma HLS INTERFACE s_axilite port=c bundle=BUS_A
#pragma HLS INTERFACE ap_hs port=a
#pragma HLS INTERFACE ap_vld port=b
#pragma HLS INTERFACE ap_none port=c register
void example(char *a, char *b, char *c)
{
#pragma HLS INTERFACE mode=s_axilite port=a bundle=BUS_A
#pragma HLS INTERFACE mode=s_axilite port=b bundle=BUS_A
#pragma HLS INTERFACE mode=s_axilite port=c bundle=OUT
#pragma HLS INTERFACE mode=s_axilite port=return bundle=BUS_A
#pragma HLS INTERFACE mode=ap_vld port=b
*c += *a + *b;
}
Notes: Ug1399 Page 264 S_AXILITE and Port-Level Protocols

## Slide 30: Controllable Register Maps in AXI4 Lite
Assigning offset to array (RAM) interfaces
  Specified value is offset to base of array
  Array’s address space is always contiguous and linear
C Driver Files include offset information
  In generated driver file xhls_sig_gen_bram2axis.h
void hls_sig_gen_bram2axis(hls::stream<axis_last_t<data_t> >& dout,
data_t sig_buf[MAX_SIG_PERIOD], short sig_period)
{
#pragma HLS INTERFACE port=return mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_buf mode=s_axilite bundle=ctrl offset=0x1000
#pragma HLS INTERFACE port=sig_period mode=s_axilite bundle=ctrl offset=0x0400
...
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_PERIOD_DATA 0x0400
...
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_BUF_BASE 0x1000
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_BUF_HIGH 0x17ff
...
Notes: Didn’t find match information

## Slide 31: Controllable Register Maps in AXI4 Lite
Assigning offset to array (RAM) interfaces
  Specified value is offset to base of array
  Array’s address space is always contiguous and linear
C Driver Files include offset information
  In generated driver file xhls_sig_gen_bram2axis.h
void hls_sig_gen_bram2axis(hls::stream<axis_last_t<data_t> >& dout,
data_t sig_buf[MAX_SIG_PERIOD], short sig_period)
{
#pragma HLS INTERFACE port=return mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_buf mode=s_axilite bundle=ctrl offset=0x1000
#pragma HLS INTERFACE port=sig_period mode=s_axilite bundle=ctrl offset=0x0400
...
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_PERIOD_DATA 0x0400
...
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_BUF_BASE 0x1000
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_BUF_HIGH 0x17ff
...
Notes: Didn’t find match information

## Slide 32: Native AXI4 Master
Interface Mode: m_axi
  Supported with INTERFACE directive
Options
  Multiple ports may be grouped into the same AXI4 Master interface
    All ports which use the same bundle name are grouped
  Depth option is required for C/RTL co-simulation
    Required for pointers, not arrays
    Set to the number of values read/written
  Option to support offset or base address
void example(volatile int *a)
{
#pragma HLS INTERFACE mode=m_axi depth=50 port=a

## Slide 33: Native AXI4 Master
Interface Mode: m_axi
  Supported with INTERFACE directive
Options
  Multiple ports may be grouped into the same AXI4 Master interface
    All ports which use the same bundle name are grouped
  Depth option is required for C/RTL co-simulation
    Required for pointers, not arrays
    Set to the number of values read/written
  Option to support offset or base address
void example(volatile int *a)
{
#pragma HLS INTERFACE m_axi depth=50 port=a

## Slide 34: Native AXI4 Master : Offset Support
Address Offset / Base Address Support
  Support provided for address offset
Port Offset
  Defines the offset for the port
  May be set on individual interfaces using the INTERFACE directive
Global Offset
  Globally controls the offset ports of all M_AXI interface in the design
  May be set using the interface configuration
    Using Tcl command config_interface -m_axi_offset option

## Slide 35: Native AXI4 Master : Offset Support
Address Offset / Base Address Support
  Support provided for address offset
Port Offset
  Defines the offset for the port
  May be set on individual interfaces using the INTERFACE directive
Global Offset
  Globally controls the offset ports of all M_AXI interface in the design
  May be set using the interface configuration
    Using Tcl command config_interface -m_axi_offset option

## Slide 36: Native AXI4 Master: Offset=off
AXI4 Master Interface
  No offset is provided for the address
    Same as existing behavior
  The offset (BASEADDR) is set IPI
    Using IP customization GUI
  The offset can not be changed on the fly
AXI4 Master Interface
config_interface -m_axi_offset off
Notes: Default offset mode in document is off, but in vits command configuration is slave
测试后应该是slave，文档描述有误

## Slide 37: Native AXI4 Master: Offset=off (default)
Default AXI4 Master Interface
  No offset is provided for the address
    Same as existing behavior
  The offset (BASEADDR) is set IPI
    Using IP customization GUI
  The offset can not be changed on the fly
AXI4 Master Interface
config_interface -m_axi_offset off
Notes: Default offset mode in document is off, but in vits command configuration is slave
测试后应该是slave，文档描述有误

## Slide 38: Native AXI4 Master: Offset=direct
Direct Interface
  Generates a scalar input offset port
  The offset is set by driving the input port
  It can be changed on the fly by driving the port with a different value
AXI4 Master Interface …
…Plus port to specify address offset
config_interface -m_axi_offset direct

## Slide 39: Native AXI4 Master: Offset=direct
Direct Interface
  Generates a scalar input offset port
  The offset is set by driving the input port
  It can be changed on the fly by driving the port with a different value
AXI4 Master Interface …
…Plus port to specify address offset
config_interface -m_axi_offset direct

## Slide 40: Native AXI4 Master: Offset=slave(Default)
Direct Interface
  Generates an offset port and automatically maps it to an AXI4 Slave Lite interface
  User must program the offset before starting transactions on the AXI4 Master interface
  It can changed on the fly by re-programming the offset register
AXI4 Master Interface …
…Plus AXI4 Slave Lite interface to program the address offset
config_interface -m_axi_offset slave

## Slide 41: Native AXI4 Master: Offset=slave(Default)
Direct Interface
  Generates an offset port and automatically maps it to an AXI4 Slave Lite interface
  User must program the offset before starting transactions on the AXI4 Master interface
  It can changed on the fly by re-programming the offset register
AXI4 Master Interface …
…Plus AXI4 Slave Lite interface to program the address offset
config_interface -m_axi_offset slave

## Slide 42: Burst Accesses Inferred for AXI4 Master
There are two types of accesses on an AXI Master
  Burst accesses are more efficient
  Burst access has until now required the use of memcpy()
Burst Accesses are now inferred
  From operations in a for-loop and from sequential operations in the code
  However: there are some limitations
    Single for-loops only, no nested loops
Single Access
Burst Access
void example(int *a)
{
#pragma HLS INTERFACE m_axi port=a depth=...
...
int val[i] = *(a + i);
...
void example(int *a)
{
#pragma HLS INTERFACE m_axi port=a depth=...
...
memcpy(vals, a, N * sizeof(int));
...

## Slide 43: AXI4-Master : Burst Access with a Single Port
Burst access with single port
  Loop must be pipelined
  Address must be accessed in increasing order
  Memory accesses cannot be guarded by a conditional statement
  Do not flatten nested loops
  Only one read and write per AXI port allowed in a for loop
  Only one read and one write is allowed in a for loop unless the ports are bundled in different AXI ports
//Port a is assigned to an AXI4 master interface
void example(volatile int *a){
#pragma HLS INTERFACE mode=m_axi port=a depth=50
#pragma HLS INTERFACE mode= s_axilite port=return
int i;
int buff[50];
//Burst data into the Design
//memcpy creates a burst access to memory
memcpy(buff,(const int*)a,50*sizeof(int));
//Perform some calculation
for(i=0;i<50;i++){
buff[i]=buff[i]+100;
}
//Burst Dara out of the design
//Alternatively, for loop creates a burst access to memory
for(i=0;i<50;i++){
#pragma HLS PIPELINE
a[i]=buff[i];
}
}

## Slide 44: AXI4-Master : Burst Access with Multiple Ports
Burst access with multiple ports
  Vitis HLS implements the port reads as burst transfers
  Port a is specified without using the bundle option and is implemented in the default AXI interface
  Port b is specified using a named bundle and is implemented in a separate AXI interface called d2_port
  In the multiple access bursts
    Only one access(read or write) per port can be inferred from a for loop
    No simultaneous read and write access
    If multiple ports are used, multiple reads or writes can be performed
//Two pointers are accessed
void example(volatile int *a, int *b){
#pragma HLS INTERFACE mode= s_axilite port=return
//Two different AXI ports are used
#pragma HLS INTERFACE mode=m_axi port=a depth=50
#pragma HLS INTERFACE mode=m_axi port=b depth=50 bundle=d2_port
int i;
int buff[50];
//Copy data in
for(i=0;i<50;i++){
#pragma HLS PIPELINE
//separate AXI ports mean both a and b reads implemented as bursts
buff[i]=a[i]+b[i];
}
…
}

## Slide 45: Burst Accesses Inferred for AXI4 Master
There are two types of accesses on an AXI Master
  Burst accesses are more efficient
  Burst access has until now required the use of memcpy()
Burst Accesses are now inferred
  From operations in a for-loop and from sequential operations in the code
  However: there are some limitations
    Single for-loops only, no nested loops
Single Access
Burst Access
void example(int *a)
{
#pragma HLS INTERFACE m_axi port=a depth=...
...
int val[i] = *(a + i);
...
void example(int *a)
{
#pragma HLS INTERFACE m_axi port=a depth=...
...
memcpy(vals, a, N * sizeof(int));
...

## Slide 46: Byte-Enable Accesses on AXI4 Master
Byte-Enable Accesses Support on AXI4 Master Interfaces
  Single bytes are now written and read
  Improved AXI4 Master performance
Improved Performance
  This code uses 8-bit data
    Previously, accessing this required reading/writing full 32-bit
    This implied a required read-modify-write behavior: Impacted performance
  Similar performance improvement when accessing struct members
    Also often implied read-modify-write behavior
  Improved Port Bundling
    Variables of different sizes can be grouped into same AXI4 Master port
void example(volatile char *a) {
#pragma HLS INTERFACE m_axi depth=50 port=a

## Slide 47: AXI4 Port Bundling
AXI4 Master and Lite Port Bundling
  The bundle options groups arguments into the same AXI4 port
  For example, group 3 arguments into AXI4-Lite port “ctrl” :
Arguments can be Bundled into AXI4 Master and AXI4 Lite ports
  If no bundle name is used a default name is used for all arguments
    All go into a single AXI4 Master or AXI4 Lite
    Default name applied if no –bundle option is used
  Group different sized variables into an AXI4 Master port
void hls_sig_gen_bram2axis(hls::stream<data_t>& dout,
data_t sig_buf[MAX_SIG_PERIOD], short sig_period)
{
#pragma HLS INTERFACE port=return mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_buf mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_period mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=dout mode=axis

## Slide 48: AXI4 Port Bundling
AXI4 Master and Lite Port Bundling
  The bundle options groups arguments into the same AXI4 port
  For example, group 3 arguments into AXI4AXI4-Lite port “ctrl” :
Arguments can be Bundled into AXI4 Master and AXI4 Lite ports
  If no bundle name is used a default name is used for all arguments
    All go into a single AXI4 Master or AXI4 Lite
    Default name applied if no –bundle option is used
  Group different sized variables into an AXI4 Master port
void hls_sig_gen_bram2axis(hls::stream<data_t>& dout,
data_t sig_buf[MAX_SIG_PERIOD], short sig_period)
{
#pragma HLS INTERFACE port=return mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_buf mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_period mode=s_axilite bundle=ctrl
#pragma HLS INTERFACE port=dout mode=axis

## Slide 49: AXI4 Stream Interface: Ease of Use
set_directive_interface –mode axis “foo” portA
Or
#pragma HLS interface mode=axis port=portA
Interface Type “axis” is AXI4 Stream
Native Support for AXI4 Stream Interfaces
  Native = An AXI4 Stream can be specified with set_directive_interface
    No longer required to set the interface then add a resource
    This AXI4 Stream interface is part of the HDL after synthesis
    This AXI4 Stream interface is simulated by RTL co-simulation

## Slide 50: AXI4 Stream Interface: Ease of Use
set_directive_interface –mode axis “foo” portA
Or
#pragma HLS interface mode=axis port=portA
Interface Type “axis” is AXI4 Stream
Native Support for AXI4 Stream Interfaces
  Native = An AXI4 Stream can be specified with set_directive_interface
    No longer required to set the interface then add a resource
    This AXI4 Stream interface is part of the HDL after synthesis
    This AXI4 Stream interface is simulated by RTL co-simulation

## Slide 51: Generate the hardware accelerator
Select Solution > Export RTL
Select Vivado IP(.zip), Vivado IP for System Generator for Vivado
Select Output Location
Change the IP Configuration
  Vendor/Library/Version/Description/Display Name/Taxonomy
Click on OK
  The IP is exported as a ZIP file that can be added to the Vivado IP catalog.
  The impl/ip folder also contains the contents of the unzipped IP.

## Slide 52: Generate the hardware accelerator
Select Solution > Export RTL
Select IP Catalog, System Generator for Vivado or design check point (dcp)
Select Vivado IP(.zip), Vivado IP for System Generator for Vivado
Select Output Location
Change the IP Configuration
  Vendor/Library/Version/Description/Display Name/Taxonomy
Click on Configuration… if you want to change the version number or other information
  Default is v1.0
Click on OK
  The IP is exported as a ZIP file that can be added to the Vivado IP catalog.
  The impl/ip folder also contains the contents of the unzipped IP.
  The directory (ip) will be generated under the impl folder under the current project directory and current solution
  RTL code will be generated, both for Verilog and VHDL languages in their respective folders

## Slide 53: Generated impl Directory
Point IP Catalog to point to the ip directory
Generated Verilog RTL Files
Header file
IP Integrator will use this file
VITIS will use this directory

## Slide 54: Generated impl Directory
Point IP Catalog to point to the ip directory
Generated Verilog RTL Files
Header file for slave interfaces
IP Integrator will use this file
XSDK will use this directory

## Slide 55: C Driver API for AXI4-Lite Interface
Notes: No such a table now

## Slide 56: Integrating the IP-XACT Hardware Accelerator in AXI System

## Slide 57: Embedded System Design using Vivado
Create a new Vivado project, or open an existing project
Invoke IP Integrator
Construct(modify) the hardware portion of the embedded design by adding the IP-XACT hardware accelerator created in Vitis HLS
Create (Update) top level HDL wrapper
Synthesize any non-embedded components and implement in Vivado
Export the hardware description(XSA File), and launch VITIS
Create a new platform project from XSA and application projects in the VITIS
Compile the software with the GNU cross-compiler in VITIS
Download the programmable logic’s completed bitstream using Xilinx Tools > Program FPGA in VITIS
Use VITIS to download and execute the program (the ELF file)

## Slide 58: Embedded System Design using Vivado
Create a new Vivado project, or open an existing project
Invoke IP Integrator
Construct(modify) the hardware portion of the embedded design by adding the IP-XACT hardware accelerator created in Vitis HLS
Create (Update) top level HDL wrapper
Synthesize any non-embedded components and implement in Vivado
Export the hardware description(XSA File), and launch XSDKVITIS
Create a new platform project from XSA software board support package and application projects in the XSDKVITIS
Compile the software with the GNU cross-compiler in XSDKVITIS
Download the programmable logic’s completed bitstream using Xilinx Tools > Program FPGA in XSDKVITIS
Use XSDKVITIS to download and execute the program (the ELF file)

## Slide 59: Summary

## Slide 60: Summary
Embedded system development flow in FPGA involves
  Developing hardware using IP Integrator and Vivado
  Developing software using VITIS
hardware accelerator provides wide support of AXI interfaces, System Generator design, and design check point(dcp)
  Use the INTERFACE directive
  The choice of hardware accelerator is a function of the C variable type (pointer, etc.)
Start with the correct C argument type
  Verify the design at the C level
  Accept the default block-level I/O protocol
  Select the port-level I/O protocol that gives the required hardware accelerator interface
  Optionally group ports

## Slide 61: Summary
Embedded system development flow in FPGA involves
  Developing hardware using IP Integrator and Vivado
  Developing software using XSDKVITIS
hardware accelerator provides wide support of AXI interfaces, System Generator design, and design check point(dcp)
  Use the INTERFACE directive
  The choice of hardware accelerator is a function of the C variable type (pointer, etc.)
Start with the correct C argument type
  Verify the design at the C level
  Accept the default block-level I/O protocol
  Select the port-level I/O protocol that gives the required hardware accelerator interface
  Optionally group ports